## Slide 1: Unit -06
PLDs

## Slide 2: Programmable Logic Device(PLDs)
• Till now we used MSI chips for designing
different logic ckts. Due to their fixed functions,
they are called as Fixed Function Ics.
• There are two more approaches to design digital
ckts.
1. ASICs (Application Specific Integrated Ckt)
2. PLDs (Programmable Logic Devices)

## Slide 3: Types of PLDs
ROMs(Read only memories)
PLAs(Programmable Logic Arrays)
PALs(Programmable Array Logics)
CPLDs(Complex Programmable Logic Devices )
FPGAs(Field Programmable Gate Arrays)

## Slide 4: PLAs(Programmable Logic Arrays) Block Diagram:
Input Buffer
I0
I1
In-1
.
.
.
OR Matrix
P0
P1
Pn-1
.
.
.
Invert/ Noninvert Matrix
S0
S1
Sn-1
.
.
.
AND Matrix
.
.
.
I0
I0’
I1
I1’
In-1
In-1’
FFs or O/P Buffer
.
.
.
S0
S0’
S1
S1’
Sn-1
Sn-1’
F0
F1
Fm-1
.
.
.

## Slide 5: Programmable Logic Arrays (PLAs)
• • •
inputs
AND array
• • •
outputs
OR array
product terms
Pre-fabricated building block of many AND/OR gates
  ”Personalized" by making or breaking connections among gates
  Both AND & OR arrays are programmable.
  Programmable array block diagram for sum of products form

## Slide 6: Design of Boolean functions using PLA
Example 1:
F0 = A + B' C'
F1 = A C' + A B
F2 = B' C' + A B
F3 = B' C + A
PLA Program Table:
1 = uncomplemented in term
0 = complemented in term
– = does not participate
1 = term connected to output
0 = no connection to output
input side:
output side:
product inputs outputs
term A B C F0 F1 F2 F3 AB 1 1 – 0 1 1 0 B'C – 0 1 0 0 0 1 AC' 1 – 0 0 1 0 0 B'C' – 0 0 1 0 1 0 A 1 – – 1 0 0 1
reuse of terms
Shared product terms among outputs
AB, B’C, AC’, B’C’, A

## Slide 7: Design of Boolean functions using PLA
Example 2: F0 = A B + A' B'
F1 = C D' + C' D
A B
A B
C D
C D
A
B
C
D
F0
F1

## Slide 8: PLA Design Example
0 1 X 0
0 1 X 0 0 0 X X
0 0 X X
D
A
B
C
minimized functions:
W = A + B D + B C
X = B C'
Y = B + C
Z = A'B'C'D + B C D + A D' + B' C D'
A B C D W X Y Z 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 1 0 0 1 0 0 0 1 1 0 0 1 1 0 0 1 0 0 1 0 0 0 1 1 0 0 1 0 1 1 1 1 0 0 1 1 0 1 0 1 0 0 1 1 1 1 0 1 1 1 0 0 0 1 0 0 1 1 0 0 1 1 0 0 0 1 0 1 – – – – – 1 1 – – – – – –
0 0 X 1
0 1 X 1 0 1 X X
0 1 X X
D
A
B
C
K-map for W
K-map for X
0 1 X 0
0 1 X 0 1 1 X X
1 1 X X
D
A
B
C
K-map for Y
Example 3: code converter
K-map for Z
0 0 X 1
1 0 X 0 0 1 X X
1 0 X X
D
A
B
C

## Slide 9: PLA Design Example (cont’d)
A B C D
W X Y Z
A
BD
BC
BC'
B
C
A'B'C'D
BCD
AD'
BCD'
minimized functions:
W = A + B D + B C
X = B C'
Y = B + C
Z = A'B'C'D + B C D + A D' + B' C D'
Code converter: programmed PLA
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 10: PLA Design Example 4: Magnitude comparator
EQ NE LT GT
A'B'C'D'
A'BC'D
ABCD
AB'CD'
AC'
A'C
B'D
BD'
A'B'D
B'CD
ABC
BC'D'
A B C D
1 0 0 0
0 1 0 0 0 0 1 0
0 0 0 1
D
A
B
C
0 1 1 1
1 0 1 1 1 1 0 1
1 1 1 0
D
A
B
C
0 0 0 0
1 0 0 0 1 1 0 1
1 1 0 0
D
A
B
C
0 1 1 1
0 0 1 1 0 0 0 0
0 0 1 0
D
A
B
C
K-map for EQ
K-map for NE
K-map for GT
K-map for LT

## Slide 11
ABC
A
B
C
A
B
C
ABC
ABC
ABC
ABC
ABC
ABC
ABC
F1
F2
F3
F4
F5
F6
A
B
C
Design of Boolean functions using PLA
Example 5:
Multiple functions of A, B, C
F1 = A B C
F2 = A + B + C
F3 = A B C
F4 = A + B + C
F5 = A xor B xor C
F6 = A xnor B xnor C

## Slide 12: PALs(Programmable Array Logics)
Only AND array is Programmable
OR array is fixed.
Not as flexible as PLA.

## Slide 13
PLD with F/Fs(Registered PAL)

## Slide 14: ROM Structure
Similar to a PLA structure but with a fully decoded AND array
  Completely flexible OR array (unlike PAL)
n address lines
• • •
inputs
decoder
2n word lines
• • •
outputs
memory array (2n words by m bits)
m data lines